## Slide 1
Microcontrollers

## Slide 2: Objectives
Introduction fundamentals and applications of microprocessors and microcomputers.
Architecture, the instruction set, and applications of 8051 microcontroller family
Basic applications of microprocessors, such as input/output, analog-digital conversion (ADC), and digital-analog conversion (DAC), and data acquisition.
Aspects of KIT Arduino
2
Ref. I. Scott Mackenzie

## Slide 3
Textbooks
I. Scott Mackenzie, Raphael C, -W, The 8051 Microcontroller, Prentice Hall, Fourth edition.
James A. Langbridge, Arduino sketches – Tools and techniques for programming , Wiley
Tống Văn On, Hoàng Đức Hải, “Họ vi điều khiển 8051”, 2001.
Nguyễn Tăng Cường, “Cấu trúc và lập trình họ VĐK 8051”, 2003

## Slide 4
Contents:
Chapter 1: Introduction to Microcontrollers
Chapter 2: 8051 microcontroller architecture
Chapter 3: C programming for 8051
Chapter 4: Arduino

## Slide 5
Chap 1. Introduction to Microcontrollers
1
1.1. Microprocessing systems
1.2. Microcontrollers
1.3. Advanced microcontrollers
1.4. Embedded systems
1.5. Numbering and coding systems
1.6. Memory

## Slide 6
Chap 1. INTRODUCTION
1

## Slide 7
1.1 Microprocessing Systems
1

## Slide 8
1.1 Microprocessing Systems
1

## Slide 9
1.1 Microprocessing Systems
1

## Slide 10
1.1 Microprocessing Systems
1

## Slide 11
1.1 Microprocessing Systems
1

## Slide 12
1.1 Microprocessing Systems
1

## Slide 13
1.1 Microprocessing Systems
1

## Slide 14
1.2 Microcontrollers
1

## Slide 15: 1.2. Microcontrollers
Microprocessor vs. Microcontroller
Microprocessor
CPU is stand-alone, RAM, ROM, I/O, timer are separate
designer can decide on the amount of ROM, RAM and I/O ports.
Expansive
Versatility
general-purpose
Microcontroller
CPU, RAM, ROM, I/O and timer are all on a single chip
fix amount of on-chip ROM, RAM, I/O ports
Highly bit addressable
for applications in which cost, power and space are critical
single-purpose

## Slide 16
1.2. Microcontrollers
1

## Slide 17: 1.3. Advanced microcontrollers
AVR microcontrollers
PIC microcontrollers
ARM architecture

## Slide 18: AVR Microcontroller

## Slide 19: AVR general features
Enhanced RISC architecture with mostly fixed – length instruction, load-store memory access and 32 general-purpose registers.
A two – stage instruction pipeline that speeds up excution
Majority of instructions take one clock cycle
Up to 10Mhz clock operation
Wide variety of on-chip peripherals, including digital I/O, ADC, EEPROM, Timers, UART, RCT timer, PWM etc.
Internal program and data memory

## Slide 20: AVR general features
In-System programmable (ISP)
Available in 8 pin to 64 pin size to suit wide variety of applications
Up to 12 times performance speedup over conventional CISC controllers
Wide operating voltage from 2.7 to 6.0 V
Simple architecture offers a small learning curve to uninitiated

## Slide 21: What does AVR RISC mean?
The acronym AVR has been reported to stand for: Advanced Virtual RISC and also for the chip’s designers: Alf-Egil Bogen and Vegard Wollan who designed the basic architecture at the Norwegian Institute of Technology.
RISC stands for Reduced Instruction Set Computer
CPU design with a reduced instruction set as well as a simpler set of instructions ()

## Slide 22: AVR architecture

## Slide 23: AVR Mega 8 features
8 Kbyte self-programming flash program memory
1-kbyte SRAM
512 byte EEFROM
6 or 8 channel 10 bit A-D converter.
Up to 16 MIPS throughput

## Slide 24: AT Mega 8 pinout

## Slide 25: Atmega 16 Features
131 instructions
32 8-bit GP registers
Throughput up to 16 MIPS
16K programmable flash (instructions)
512 Bytes EEPROM
1K internal SRAM
Timers, serial and parallel I/O, ADC

## Slide 26: AVR memory
Flash: machine instructions go here
SRAM: for runtime data
  Note bus independence for data and instructions
EEPROM: secondary storage
  EEPROM and Flash memories have a limited lifetime of erase/write cycles

## Slide 27: PIC microtrontroller
PIC stands for Peripherals Interface Controller
The general instruments used the acronyms Programmable Interface Controller and Programmable Intelligent Computer for the initial PICs (PIC 1640 and PIC 1650)
In 1993, Microchip Technology launched the 8-bit PIC 18F84 with EEPROM which could be programmable using serial method
The improved version of PIC16c84 with flash memory (PIC18F84 and PIC18F84A) hit the market in 1998

## Slide 28: Development
Since 1998, Microchip Technology continuously developed new high performance microcontrollers with new complex architecture and enhanced in-built peripherals.
PIC microcontroller is based on Harvard architecture.
At present PIC microcontrollers are widely used for industrial purpose due to its high performance ability at low power consumption.
It is also very famous among hobbyists due to moderate cost and easy availability of its supporting software and hardware tools like compilers, simulators, debuggers, etc…

## Slide 29: Development
The 8-bit PIC microcontroller is divided into following four categories on the basic of internal architecture:
  Base line PIC
  Mid-range PIC
  Enhanced Mid-range PIC
  PIC18

## Slide 31: PIC microcontrollers
Architecture
  PIC microcontrollers are based on advanced RISC architecture
  RISC stands for Reduced Instruction Set Computing
  In this architecture, the instruction set of hardware gets reduced with increases the execution rate (speed) of system.
  PIC microcontrollers follow Harvard architecture for internal data transfer
  In Harvard architecture there are two separate memories for program and data
  These two memories are accessed through different buses for data communication between memories and CPU core.

## Slide 32: PIC microcontrollers
Architecture
  This architecture improves the speed of system over Von Neumann architecture in which program and data are fetched from the same memory using the same bus
  PIC18 series controllers are based on 16 bit instruction set
  The question may arise that if PIC18 are called 8-bit microcontrollers, then what about them being based on 16 bit instructions set.
  PIC18 is an 8bit microcontroller this statement means that the CPU core can receive/transmit or process a maximum of 8bit data at a time

## Slide 33: PIC microcontrollers
Architecture
  On the other hand the statement PIC18 microcontrollers are based on 16 bit instruction set’s means that the assembly instruction sets are of 16 bit
  the data memory is interfaced with 8 bit bus and program memory is interfaced with 16 bit bus as depicted in the following figure

## Slide 34: PIC microcontrollers
PIC18 Harvard Architecture

## Slide 35: PIC microcontrollers

## Slide 36: PIC microcontrollers
Arithmetic Logic Unit (ALU)
  Instruction decoder
    16 bits instructions
  Status register that stores flags
    5 bits
  WREG-working register
    8bit accumulator
Registers
  Program counter (PC)
    21 bit register that hold the Program Memory address
  Bank select Register (BRS)
    4 bit register used in direct addressing the Data Memory
  File select registers (FSRs)
    12 bit registers used as memosy pointers in indirect addressing Data memory

## Slide 37: PIC microcontrollers
Address bus
  21 bit address bus for Program Memory
    Addressing capacity: 2MB
  12 bit address bus for data memory
    Addressing capacity : 4KB
Data bus
  16 bit instruction/data bus for program memory
  8bit data bus for data memory
PIC18F452/4520 Memory
  Program memory: 32k
  Data memory: 4K
  Dara EEPROM:
    Not part of the data memory spave
    Addressed through special function registers

## Slide 38: PIC microcontrollers
Specical feature
  Slepp mode
  Watchdog timer
  Code protection
  In-circuit serial programming
  In circuit debugger

## Slide 39: AVR microcontroller
The ARM is a 32 bit reduced instruction set computer (RISC) developed by ARM holdings.
It was known as the Advanced RISC Machine

## Slide 40: ARM Partnership Model

## Slide 41: Introduction
Leading provider of 32 bit embdded RISC microprocessors , 75% of market.
  High performance
  Low power consumption
  Low system cost
Solutions for:
  Embedded read-time systems for mass storage, automotive, industrial and networking applications.
  Secure applications – smartcards and SIMs
  Open platforms running complex operating systems Low system cost

## Slide 42: Introduction
ARM v1:
  First version of ARM processor
  26-bit addressing, no multiply/coprocessor
ARM v2:
  First commercial chip
  Included 32-bit result multiply instructions/coprocessor support
ARM v2a:
  ARM3 chip with on-chip cache
  Added load and store cache management
ARM v3:
  ARM6, 32 bit addressing, virtual memory support

## Slide 43: ARM core diagram

## Slide 44: The registers
ARM has 37 registers all of which are 32 bits long
The current processor mode govern which of several banks is accessible. Each mode can access
  a particular set of r0-r12 registers
  a particular r13 (the stack pointer, sp) and r14 (the link register)
  The program counters, r15 (pc)
  the current program status registers, cpsr
Privileged mode (except system ) can also access
  A particular spsr (saved program status register)

## Slide 45: ARM Applications

## Slide 46: ARM cortex M applications
Dell E4300 Latitude Laptop
instant boot-up for users and access to select applications, with multi-day battery lifetimes

## Slide 47: ARM cortex A applications

## Slide 48: ARM cortex R applications

## Slide 49: Real life applications
Complete Navigation application
c bitfields
Car radio control
DES Encryption/Decryption
Three different modules from analog telephones
Battery charge
Embedded Web server

## Slide 50
1.4. Embedded system
1

## Slide 51
1.4. Embedded system
1

## Slide 52
1
1.5. Numbering and coding systems

## Slide 53
1.5. Numbering and coding systems
1

## Slide 54
1
1.5. Numbering and coding systems

## Slide 55
1
1.5. Numbering and coding systems

## Slide 56
1
1.5. Numbering and coding systems

## Slide 57
1
1.5. Numbering and coding systems

## Slide 58
1
1.5. Numbering and coding systems

## Slide 59
1
1.5. Numbering and coding systems

## Slide 60
1
1.5. Numbering and coding systems

## Slide 61
1
1.5. Numbering and coding systems

## Slide 62
1
1.6. Memory

## Slide 63
1.6. Memory
1

## Slide 64
1
1.6. Memory